## Slide 1
.
DEPARTMENT OF INFORMATION TECHNOLOGY
NOISE POLLUTION MONITORING
Team name : Proj_224788_Team_5
Team members :
Sneha V(113321205049)
Dharshini K(113321205011)
Agnal Cajolin X.I(113321205003)
Sharmila V(113321205047)

## Slide 2
Noise Sensor (Microphone):
  A basic microphone or sound sensor that can detect sound levels in the environment.
Microcontroller:
  A microcontroller, such as an Arduino or an ESP8266/ESP32, to interface with the sensor and handle data processing.
Power Supply:
  A stable power supply, which can be provided using batteries or a USB power source.
Wi-Fi Module (Optional):
  To enable the device to connect to the internet and transmit data, you can add a Wi-Fi module. Many ESP8266/ESP32 boards come with built-in Wi-Fi capabilities.
Data Storage (Optional):
  A simple SD card or EEPROM storage for logging data if you want to store historical noise level information on the device itself.
Enclosure:
  A protective casing to shield the components from environmental factors.
Connectivity Cables:
  Necessary cables and connectors to connect the microphone and other components.
Programming Interface:
  A means to program the microcontroller, such as a USB-to-serial adapter.
The Components that are required are:

## Slide 3
The Python script for noise monitoring:
import os
import time
import numpy as np
import pyaudio
import requests
# Constants for your configuration
API_ENDPOINT = 'https://your-api-endpoint.com/noise-data'
SAMPLE_RATE = 44100 # Audio sample rate (Hz)
RECORD_SECONDS = 5 # Duration of each recording (seconds)
# Initialize PyAudio
p = pyaudio.PyAudio()
def record_audio():
print("Recording audio...")
stream = p.open(format=pyaudio.paInt16, channels=1, rate=SAMPLE_RATE, input=True, frames_per_buffer=1024)
frames = []
for _ in range(0, int(SAMPLE_RATE / 1024 * RECORD_SECONDS)):
data = stream.read(1024)
frames.append(data)
stream.stop_stream()
stream.close()
audio_data = b''.join(frames)
return audio_data

## Slide 4
def main():
while True:
audio_data = record_audio()
# Calculate noise level (you can use a more complex algorithm)
noise_level = np.frombuffer(audio_data, dtype=np.int16).max()
print(f"Noise level: {noise_level} dB")
# Send data to the server
payload = {
"noise_level": noise_level
}
try:
response = requests.post(API_ENDPOINT, json=payload)
if response.status_code == 200:
print("Data sent successfully.")
else:
print(f"Failed to send data. Status code: {response.status_code}")
except Exception as e:
print(f"Failed to send data: {str(e)}")
time.sleep(60) # Wait for 1 minute before taking the next reading
if __name__ == '__main__':
main()

## Slide 5
In conclusion, an IoT device for noise pollution monitoring is a valuable tool in addressing the growing concern of noise pollution in urban and industrial environments. Such devices can provide real-time data, enabling informed decisions for mitigating the effects of noise pollution.
CONCLUSION :